## Slide 1: Assembly Lang. – Intel 8086 Addressing modes – 1
The way in which an operand is specified is called the Address Mode.

## Slide 2
Flexible access to memory, allowing you to easily access variables, arrays, records, pointers, and other complex data types.
Mastery of the 80x86 addressing modes is the first step towards mastering 80x86 assembly language.

## Slide 3
x86 instructions use five different operand types:
registers,
constants, and
three memory addressing schemes.
Each form is called an addressing mode.
http://www.electronics.dit.ie/staff/tscarff/8086_address_modes/8086_address_modes.htm

## Slide 4: x86 processors support 
the register addressing mode ,
the immediate addressing mode,
the direct addressing mode,
the indirect addressing mode,
the base plus index addressing mode,
the register relative addressing mode, &
the base relative plus index addressing mode.

## Slide 5: 1. Register AM
      mov ax, ax
      mov ax, bx
      mov ax, cx
      mov ax, dx
The first instruction accomplishes absolutely nothing. It copies the value from the ax register back into the ax register.
The remaining three instructions copy the value of bx, cx and dx into ax.
Note that the original values of bx, cx, and dx remain the same.
The first operand (the destination) is not limited to ax; you can move values to any of these registers.

## Slide 6
By specifying the name of the register as an operand to the instruction, you may access the contents of that register.
    mov AX, BL  ok?
The eight and 16 bit registers are certainly valid operands for this instruction. The only restriction is that both operands must be the same size.

## Slide 7
mov ax, bx ;Copies the value from BX into AX
mov dl, al ;Copies the value from AL into DL
mov si, dx ;Copies the value from DX into SI
mov sp, bp ;Copies the value from BP into SP
mov dh, cl ;Copies the value from CL into DH
mov ax, ax ;Yes, this is legal!

## Slide 8: 2. Immediate AM – constant
        mov ax, 25
        mov bx, 195
        mov cx, 2056
        mov dx, 1000
These instructions are all pretty straightforward.
 They load their respective registers with the specified hexadecimal constant.

## Slide 9
There are three addressing modes which deal with accessing data in memory. These addressing modes take the following forms:
mov ax, [1000]
mov ax, [bx]
mov ax, [1000+bx]

## Slide 10: Direct [memory] AM – operand is variable
mov ax, [1000]
uses the direct addressing mode to load ax
 with the 16 bit value
 stored in memory
 starting at location 1000 hex.

## Slide 11: Indirect [mem] AM
mov ax, [bx]
It loads ax from the memory location specified by the contents of the bx register.
This is an indirect addressing mode.
Rather than using the value in bx, this instruction accesses to the memory location whose address appears in bx.
 Pointer of the memory location [C prog.]

## Slide 12
mov bx, 1000
mov ax, [bx]
are equivalent to the single instruction:
mov ax, [1000]

## Slide 13: Base + index AM
mov ax, [1000+bx]
This instruction adds the contents of bx with 1000 to produce the address of the memory value to fetch.
This instruction is useful for accessing elements of arrays, records, and other data structures.

## Slide 14: 8086 AM

## Slide 16: Marut – 10.2.2 Based & Indexed AM
Offset address is obtained by adding a number called displacement to the contents of a register.
Displacement 
  Offset address of a variable
  A constant +/-
  The offset address of a variable +/- a const.

## Slide 17: Syntax of an operand~
[reg. + displacement]
[displacement + reg]
[reg] + displ
dipl. + [reg.]
displ[reg]
Reg. must be
BX, SI or DI  DS contains the segment no. of the operand’s address
BP  SS has the segment no.

## Slide 18: Based/Indexed
AM is Based  if BX (base reg) or, BP (base pointer) is used.
AM is indexed  if SI (source index) or, DI (destination index) is used.
e.g., W is a word array, BX contains 4.
MOV AX, W[BX]
The displacement is the offset address of variable W.
The instruction moves the element at address W+4 to AX. This is the 3rd element in the array.

## Slide 19: Other forms of previous example…
  MOV AX, W[BX]
  MOV AX, [W+BX]
  MOV AX, [BX+W]
  MOV AX, W+[BX]
  MOV AX, [BX]+W

## Slide 20: Indexed – SI source index or DI dest index
E.g., suppose SI contains the address of a word array W. Instruction –
  MOV AX, [SI+2] ;displ is 2
  The instruction moves the contents of W+2 to AX.
  This is the 2nd element of the array
  Other forms:

## Slide 21: Other forms
    MOV AX, [SI+2] ;displ is 2
    MOV AX, 2+[SI]
    MOV AX, [SI]+2
    MOV AX, [SI+2]
    MOV AX, 2[SI]

## Slide 22: Q. Write some code to sum in AX the elements of an array.
Idea is to set a pointer to the base of the array,
& let it move up the array,
& summing elements as it goes.
XOR AX, AX ;AX holds sum
LEA SI, W ;SI points to array W
MOV CX, 10 ;CX has no. of elements
ADDARRAY:
ADD AX, [SI] ;sum=sum + element
ADD SI, 2 ;move pointer to the next element
LOOP ADDARRAY ;loop until done
loop

## Slide 23
This is done by  Register indirect AM.
Add 2 as it is WORD not BYTE array
LEA moves the source offset address – into the destination.

## Slide 24: The same - using based AM
Based AM – BX [base reg] or BP [base pointer]
The idea is to cleat BX – then add 2 to it on each trip – through summation loop.
XOR AX, BX ;AX holds sum
XOR BX, BX ;clear base reg BX
MOV CX, 10 ;CX has no. of elements
ADDARRAY:
ADD AX, W[BX] ;sum=sum+element
ADD BX, 2 ;index next element
LOOP ADDARRAY ;loop until done

## Slide 25: LEA – Load effective address
Loads an offset memory address to a register
LEA destination, source
The offset address of the source memory operand is placed in the destination, which is a general register.

## Slide 26: LOOP
LOOP
CX is decremented by 1,
  If the result is not zero, then control is transferred to the labeled instruction;
  Else, control flows to the next instruction
  Flags affected – none

## Slide 27: 8086 Memory Addressing Modes
The 8086 provides 17 different ways to access memory! 17!!
But – variants of one another.
5 basics are –
displacement-only,
base,
displacement + base,
base + indexed, and
displacement + base + indexed.
http://www.ic.unicamp.br/~celio/mc404s2-03/addr_modes/intel_addr.html

## Slide 28: I. Displacement Only Addressing Mode
displacement-only (or direct) addressing mode consists of a 16 bit constant that specifies the address of the target location.
mov al, ds:[8088h] loads the al register with a copy of the byte at memory location 8088h.
Likewise, the instruction mov ds:[1234h],dl stores the value in the dl register to memory location 1234h:

## Slide 29
Indexed addressing uses a register (implicitly or explicitly) as an offset, which is added to the address in the operand to determine the effective address of the data.
Based addressing is similar except that a base register is used instead of an index register.
The difference between these two is that an index register holds an offset relative to the address given in the instruction, a base register holds a base address where the address field represents a displacement from this base.

## Slide 30: Pipelining
Some CPUs divide the fetch-decode-execute cycle into smaller steps.
These smaller steps can often be executed in parallel to increase throughput.
Such parallel execution is called instruction-level pipelining.
This term is sometimes abbreviated ILP in the literature.