## Slide 1: Microcontroller – 2 PIC

## Slide 2: Various companies
Freescale semiconductor’s –x Motorola] 68HC11
Intel – 8051
Atmel – AVR
Zilong – Z8
Microchip technology – PIC
etc.

## Slide 3: PIC – Peripheral Interface Controller by Microchip Tech. Corp.
Peripheral?
Interface?
Controller?

## Slide 4: PIC Microcontrollers
Peripheral Interface Controller (PIC) was originally designed by General Instruments
In the late 1970s, GI introduced PIC® 1650 and 1655 – RISC with 30 instructions.
PIC was sold to Microchip
Features: low-cost, self-contained, 8-bit, Harvard structure, pipelined, RISC, single accumulator, with fixed reset and interrupt vectors.

## Slide 5: PIC Families
PIC Family | Stack Size | Instruction Word Size | No of Instructions | Interrupt Vectors
12CX/12FX | 2 | 12- or 14-bit | 33 | None
16C5X/16F5X | 2 | 12-bit | 33 | None
16CX/16FX | 8 | 14-bit | 35 | 1
17CX | 16 | 16-bit | 58 | 4
18CX/18FX | 32 | 16-bit | 75 | 2
‘C’ implies CMOS technology; Complementary Metal Oxide Semiconductor
‘F’ insert indicates incorporation of Flash memory technology
Example: 16C84 was the first of its kind. It was later reissued as the 16F84, incorporating Flash memory technology. It was then reissued as 16F84A.

## Slide 6: 12 Series PIC
The small 12F508

## Slide 7: PIC 12F508/509 pin connection diagram

## Slide 8: The 12F508 Architecture

## Slide 9: Microchip is the no. 1 supplied of 8-bit microcontrollers!
8 pins
Small Data RAM
Few hundred bytes of on-chip (program [code]) ROM
One timer
Few pins for I/O ports
8-bit processor – CPU can work on only 8-bits of data at a time
Q: if data is larger than 8 bits?
 Break it into 8-bit pieces to be processed by the CPU

## Slide 10: PIC… - Upwardly compatible in terms of software, when going from one family to another family?
Not always – prob!
E.g.,
  PIC12xxx has 12-bit wide instructions
  PIC16xxx has 14-bit wide instructions
  PIC18xxx has 16-bit wide instructions & many new instructions
  *So, to run a prog in PIC18 – but written for PIC12
  – we MUST recompile the prog, &
  – possibly change some register locations before loading it into the PIC18.

## Slide 11: PIC18xxx
Highest-performance 8-bit microcontroller
~ 18- to 80-pin packages
Now, no 8-pin versions of PIC18 [others have]
Q. RISC or CISC architecture?
  RISC!

## Slide 12: PIC18
RISC
Data RAM
On-chip (program [code]) ROM
Data EEPROM - Q. What is EEPROM?
  I/O ports
Peripherals – e.g.,
  Timers
  ADC – Q. What is ADC?
  USART - Universal Asynchronous Receiver/Transmitter

## Slide 13: Read
Simplified view of a PIC microcontroller
PIC18, PIC16 block diagrams

## Slide 14: ROM – why?
To store programs
– hence, called program/code ROM
PIC18 has 2MB of prog ROM space
This ROM type may be of –
  Flash
  OTP
  Masked
  [more in Ch. 14]

## Slide 15: PIC mcc with UV-EPROM
Need PROM burner
Need UV-EPROM eraser to erase the contents of ROM
The window of the U…M chip allows the UV light to erase the roM
~20min to erase the chip before it can be programmed again
hence, need flash version of the PIC family
[see Table 1-2]

## Slide 16: PIC18Fxxx with flash memory
F – for flash
Flash version can erase in seconds
Need a ROM burner that supports flash mem
But a ROM eraser is not needed, as flash is an EEPROM [electrically-

## Slide 17
An embedded system is a product that has one or more computers embedded within it, which exercise primarily a control function.
The embedded computer is usually a microcontroller: a microprocessor adapted for embedded control applications.
Microcontrollers are designed according to accepted electronic and computer principles, and are fundamentally made up of microprocessor core, memory and peripherals.

## Slide 18
Microchip offers a wide range of microcontrollers, divided into a number of different families. Each family has identical central architecture and instruction set. However, common features also appear across all their microcontrollers.
The Microchip 12F508 is a good microcontroller to introduce a range of features of microcontrollers in general and of PIC microcontrollers in particular.